Contents

Introduction

1	Scope

2	References

3	Terms, conditions and abbreviated terms

4	Subsystems common services
4.1	Introduction
4.2	Telecommand Boot Count Service (service <number here>)
4.3	Telecommand Event Log Request Service (service <number here>)
4.4	Telecommand Set Time Service (service <number here>)
4.5	Telecommand Subsystem Reset Service (service <number here>)

5	Electrical Power Subsystem services
5.1	Health Report service
5.2	Burn Antenna service
5.3	Subsystem power control service
5.4

6	Atitude Determination and Control Subsystem services
6.1	Health Report service
6.2
6.3
6.4

7	Communication Subsystem services
7.1	Health Report service
7.2
7.3
7.4
# Introduction

The LSF-SDD-* series of documents are ment to describe the communication format between the various subsystems aboard a cubesat. The various functions supported and executed by the cubesat are implemented in the form of software services as recommented from ECSS, The European Cooperation for Space Standardization and these standards and recommentations has been followed where possible and extended to mission specific areas, also followed practices from other cubesat missions has been taken into account.

# 1 Scope
This documents describes the minimal services that every subsystem across a cubesat should be able to generate a service report following a service request (services are used in accordance with their specification on reference document [i] )
# 2 References

1. ECSS-E-70-41A (30Jan2003)

# 3 Terms, conditions and abbreviated terms

# 4 Subsystems common services

## 4.1 Introduction

The following commands are to be implemented from every subsystem on board the gr02UPSat. The packet structure (headers and data fields) for every command is displayed in this paragraph.

### 4.1.1 Telecommand packet structure
Packet Header (48 bits)					Packet Data Field (Variable bits)
Packet ID				Packet Sequence Control		Packet Length	Data Field Header (Optional see Note1)	Application Data	Spare	Packet Error Control (see Note 2)
Version Number (=0)	Type (=1)	Data Field Header Flag	Appliation Process ID
3	1	1	11	2	14
16				16		16	Variable	Variable	Variable	16

Figure 1: Telecommand packet fields
- NOTE 1, see note 1 on reference [i], page 42.
- NOTE 2, see note 1 on reference [i], page 43.
For more information regarding the individual segments of the frame see reference [i], page 42.

### 4.1.2 Telemerty source packet structure
Packet Header (48 bits)					Packet Data Field (Variable bits)
Packet ID				Packet Sequence Control		Packet Length	Data Field Header (Optional see Note1)	Source Data	Spare (Optional)	Packet Error Control (Optional)
Version Number (=0)	Type (=0)	Data Field Header Flag	Appliation Process ID	Grouping Flags	Source Sequence Control
3	1	1	11	2	14
16				16		16	Variable	Variable	Variable	(see Note 2)

Figure 2: Telemetry packet fields
- NOTE 1, see note 1 on reference [i], page 46.
- NOTE 2, see note 1 on reference [i], page 46.

### 4.1.3 Service data units
A service request or report contains the SourceData field, which is composed from the actual data called 'Service data units' that is relevant to the specific service function. The general format of a service data unit is presented next:
Parameter1	Parameter2	Parameter3
<type>	<type>	<type>

supported types are presented on reference [i], page 42.

## 4.2 Telecommand Boot Count Service
### 4.2.1 Scope / Service concept
This service request instructs the receiving subsystem to generate a service report with data payload containing the boot counter, the boot counter response contains how many times the subsystem has suffer a reset ( a counter incremented on every boot and stored localy on the subsystem )
The service data unit format is the following:
Parameter1
Unsigned Integer

### 4.2.2 Service Requests and reports
Requests:
BootCounter
0

- BootCounter:
  - Type of: 1 bit long.
  - Description: the zero bit to initiate a service request from the receiving subsystem.
Reports:
BootCounter
Unsigned Integer / 4 octets

- BootCounter:
  - Type of: uint32.
  - Description: 32 bit long integer.

### 4.2.3 Service capability sets
Minimum Capability set:
Subtype	Service request, report or capability
1
2

## 4.3 Telecommand Event Log Request Service
### 4.3.1 Scope / Service concept
This service request instructs the receiving subsystem to generate a service report with data payload containing the Event log that the subsystem is retains on memory. Every subsystem without individual storage should keep important events on memory and be able to pass them on a requesting service (eg. for OBC to save them on the SDCard)
The service data unit format is the following:
Parameter1

### 4.3.2 Service Requests and reports
Requests:
0

Reports:

### 4.3.3 Service capability sets
Minimum Capability set:
Subtype	Service request, report or capability
1
2

## 4.4 Telecommand Set Time Service
### 4.4.1 Scope / Service concept
This service request instructs the receiving subsystem to update his subsystem time. All times on cubesat subsytems are epoch from 2000.
The service data unit format is the following:
TimeSet
time in seconds

### 4.4.2 Service Requests and reports
Requests:
TimeSet
time in seconds

- TimeSet:
  - Type of: unsigned long int.
  - Description: the epoch from year 2000 in seconds.
Reports:

### 4.4.3 Service capability sets
Minimum Capability set:
Subtype	Service request, report or capability
1
2

## 4.5 Telecommand Subsystem Reset Service
### 4.5.1 Scope / Service concept
This service request instructs the receiving subsystem to perform a reset on its self.
After successfull reboot a service report should be generated from the subsystem?
The service data unit format is the following:
Reset
0

### 4.5.2 Service Requests and reports
Requests:
Reset
0

- Reset:
  - Type of: bit.
  - Description: the zero bit, instructing to perform a reset.
Reports:
Reset
1

- Reset:
  - Type of bit.
  - Description: the 1 bit, reporting that the a reset has been executed.
### 4.5.3 Service capability sets
Minimum Capability set:
Subtype	Service request, report or capability
1
2

# 5 Electrical Power Subsystem services
## 5.1 Health Report service
### 5.1.1 Scope / Service concept
This service request instructs the receiving subsystem generate a service report containing various parameters about its state.
The service data unit format is the following:
HealthExtReport	PanelStats	Battery TempSensorState	StateReport
7 bits per solar panel	? bits	1 bit	1 octet

### 5.1.2 Service Requests and reports
Requests:
GenerateReport
0

- GenerateReport:
  - Type of: bit.
  - Description: the zero bit, instructing to generate the report.
Reports:
HealthExtReport	PanelStats	Battery TempSensorState	StateReport
7 bits per solar panel	? bits	1 bit	1 octet

- HealthExtReport:
  - Type of: bit.
  - Description: 7 bits per solar panel giving status about it?.
- PanelStatus:
  - Type of: bit
  - Description: ? bits, one per panel for working state, where 0 is normal working state.
### 5.1.3 Service capability sets
Minimum Capability set:
Subtype	Service request, report or capability
1
2

## 5.2 Burn Antenna service
### 5.2.1 Scope / Service concept
This service request instructs the receiving subsystem generate a service report after completing the specified system antennas fillament burn.
The service data unit format is the following:
IntervalToExecuteCommand	Subsystem
time in seconds	enumerated

### 5.2.2 Service Requests and reports
Requests:
IntervalToExecuteCommand	Subsystem
integer	bit

- IntervalToExecuteCommand:
  - Type of: uint8.
  - Description: allows interval up to 256 seconds.
- Subsystem:
  - Type of: bit
  - Description: 0 for Communication subsystem antennas, 1 for Science unit antennas.
Reports:
As standard service type 1
### 5.2.3 Service capability sets
Minimum Capability set:
Subtype	Service request, report or capability
1
2

## 5.3 Subsystem power control service
### 5.3.1 Scope / Service concept
This service request instructs the receiving subsystem generate a service report after completing the specified command related to powering on/off specific subsystems of the cubesat.
The service data unit format is the following:
Subsystem	Action
enumerated	enumerated

### 5.3.2 Service Requests and reports
Requests:
Subsystem	Action
3 bits	1 bit

- Subsystem:
  - Type of: bit.
  - Description: 00 for total shutdown, 01 for OBC, 10 for SU, 11 for COMMS.
- Action:
  - Type of: bit
  - Description: 0 to power up, 1 to power off.
Reports:
As standard service type 1
### 5.3.3 Service capability sets
Minimum Capability set:
Subtype	Service request, report or capability
1
2

# 6 Attitude Determination and Control Subsystem services
## 6.1 Health Report service
### 6.1.1 Scope / Service concept
This service request instructs the receiving subsystem generate a service report containing various parameters about its state.
The service data unit format is the following:
SpinTorquer	IMU	Coils	Magneto	Temperature	Vpp	PosFix

### 6.1.2 Service Requests and reports
Requests:
GenerateReport
0

- GenerateReport:
  - Type of: bit.
  - Description: the zero bit, instructing to generate the report.
Reports:
SpinTorquer	IMU	Coils	Magneto	Temperature	Vpp	PosFix	TIme

- SpinTorquer:
  - Type of:
  - Description:
- IMU:
  - Type of: ?
  - Description: ?
- Coils:
  - Type of: ?
  - Description: ?
- Magneto:
  - Type of: ?
  - Description: ?
- Temperature:
  - Type of: ?
  - Description: ?
- Vpp:
  - Type of: ?
  - Description: ?
- PosFix:
  - Type of: ?
  - Description: ?
- Time:
  - Type of: ?
  - Description: ?
Reports:
## As standard service type 1
## 6.2 GPSPwrCtrl service
### 6.2.1 Scope / Service concept
This service request instructs the receiving subsystem generate a service report after completing the specified command related to powering on/off the GPS.
The service data unit format is the following:
SpinTorquer	IMU	Coils	Magneto	Temperature	Vpp	PosFix

### 6.2.2 Service Requests and reports
Requests:
GPSPWRMODE
0

- GPSPWRMODE:
  - Type of: bit.
  - Description: 0 for power up, 1 for power off.
Reports:
As standard service type 1
### 6.1.3 Service capability sets
Minimum Capability set:
Subtype	Service request, report or capability
1
2

# 7 Communication subsystem services
## 7.1 Health Report service
### 7.1.1 Scope / Service concept
This service request instructs the receiving subsystem generate a service report containing various parameters about its state.
The service data unit format is the following:
Temprature	PowerAmpsOverTemp	RSSI RX	Reset Count	SystemState

### 7.1.2 Service Requests and reports
Requests:
GenerateReport
0

- GenerateReport:
  - Type of: bit.
  - Description: the zero bit, instructing to generate the report.
Reports:
Temprature	PowerAmpsOverTemp	RSSI RX	Reset Count	SystemState

- Temprature:
  - Type of:
  - Description:
- PowerAmpsOverTemp:
  - Type of: ?
  - Description: ?
- RSSI RX:
  - Type of: ?
  - Description: ?
- ResetCount:
  - Type of: ?
  - Description: ?
- SystemState:
  - Type of: ?
  - Description: ?
Reports:
## As standard service type 1
## 7.2 SetRate service
### 7.2.1 Scope / Service concept
This service request instructs the receiving subsystem generate a service report after completing the specified command related to setting the TX/RX rate of the communication subsystem.
The service data unit format is the following:
Subsystem	Speed
enumerated	enumerated

### 7.2.2 Service Requests and reports
Requests:
Subsystem	Speed
bit	bit

- Subsystem:
  - Type of: bit.
  - Description: 0 to set tx rate, 1 to set rx rate.
- Speed:
  - Type of: bit
  - Description: to be decided, etc 001 fro 1200bps
Reports:
As standard service type 1
### 7.1.3 Service capability sets
Minimum Capability set:
Subtype	Service request, report or capability
1
2

## 7.3 SetTXPower service
### 7.3.1 Scope / Service concept
This service request instructs the receiving subsystem generate a service report after completing the specified command related to setting the transmission power of the communication subsystem.
The service data unit format is the following:
Power
integer

### 7.3.2 Service Requests and reports
Requests:
Power
integer

- Power:
  - Type of: uint8.
  - Description: the tx power to be set.
Reports:
As standard service type 1
### 7.3.3 Service capability sets
Minimum Capability set:
Subtype	Service request, report or capability
1
2

## 7.4 SetRXTXState service
### 7.4.1 Scope / Service concept
This service request instructs the receiving subsystem generate a service report after completing the specified command related to setting the transmission switch on or off communication subsystem.
The service data unit format is the following:
State
bit

### 7.4.2 Service Requests and reports
Requests:
State
2 bits

- State:
  - Type of: bit
  - Description: the state are as follows:
00	TX ON
01	TX OFF
10	RX ON
11	RX OFF

Reports:
As standard service type 1
### 7.4.3 Service capability sets
Minimum Capability set:
Subtype	Service request, report or capability
1
2