###### Communication between subsystems

For communications between the subsystems, through the uart, a part of the HLDLC protocol will be used with byte stuffing, for more information check the asynchronous framing section in the link.

Byte Stuffing Info ( only applicable to UART/USART comms )
The start flag will be the 0x7E and the control escape flag 0x7D. Each frame should start and end with the start flag.

References:
[1] ECSS-E-70-41A	(30Jan2003)

Service implementation table

---------------------------------------------------------------	Process name and assigned APID	Service, subtype / (X,Y) form	---------------------------------------------------------------	---------------------------------------------------------------
Subsystem	---------------------
COMMS
-//-
-//-
EPS
-//-
-//-
OBC
-//-
-//-
ADCS
-//-
-//-
SU
-//-
-//-
IAC
-//-
-//-
Ground(?)

Interesting Services Table

Service Name	Service No.	Brief. Explanation	Implementation Candidate
Telecommand Verification Service	1	see ref. [1], page 51. / Maybe to implement basic subtypes.	obc routing proce

Device command distribution service	2		more likely none
Housekeeping and diagnostic data reporting service	3	see ref. [1], page 64. / To be implemented to some extend.
Parameter statistics reporting service	4	see ref. [1], page 73. / Maybe to implement basic subtypes will allow us to save some space/time on telemetry reporting	obc
Event reporting service	5	see ref. [1], page 79.	obc
Memory management service	6	see ref. [1], page 83.	more likely none
Function management service	8	see ref. [1], page 91.	any APID which performs functions onboard
Time management service	9	see ref. [1], page 97.	To do a custom subtype capable to set time from ground station in case GPS gets messed up and leaves us blind.
On-board operations scheduling service	11	see ref. [1], page 99 and 32.	obc
On-board monitoring service	14	see ref. [1], page 119.
Large data transfer service	13	see ref. [1], page 135
Packet forwarding control service	14	see ref. [1], page 145, 35
On-board storage and retrieval service	15	see ref. [1], page 153
Test service	17	see ref. [1], page 167
On-board operations procedure service	18	see ref. [1], page 169
Event action service	19	see ref. [1], page 177

###### Service 3, Housekeeping and diagnostic data reporting service.
Brief Exp: The subsystems implementing this service as a whole or some subtypes of it, must be able to produce the following messages per subtype:

###### subtype 21

SID
8 bits

###### subtype, 23

SID	N	Parameter#
8 bits	8 bits	enumerated

NAME	APP ID	SID	N	Par1	Par2.1-10	Par2.2
Event / report	Generic	2: events	MAX 10 events	Num of overuns / 8 bits	Event / 8 bits	time in QB50 epoch

NAME	APP ID	SID	N	Par1	Par2	Par3	Par4	Par5	Par6
Health / report	EPS	1: health report	6	batt volt / 8 bits	batt cur / 8 bits	3v3 bus current / 8 bits	5v bus current / 8 bits	TEMP 8 bits	TEMP batt / 8 bits

NAME	APP ID	SID	N	Par1	Par2	Par3
Health / report	EPS	2: extended health report		batt volt	batt cur

NAME	APP ID	SID	N	Par1
Health / report	COMMS	1: health report	1	Temp / 8 bit

NAME	APP ID	SID	N	Par1
Health / report	OBC	3: extended health report	1	time in QB50 epoch

NAME	APP ID	SID	N	Par1	Par2	Par3	Par4	Par5	Par6	Par7	Par8
WOD / report	OBC	4: WOD report	8	Mode / 1 bit	batt volt / 8 bits	batt cur / 8 bits	3v3 bus current / 8 bits	5v bus current / 8 bits	TEMP COMMS 8 bits	TEMP / EPS / 8 bits	TEMP batt / 8 bits

###### even though the service intends the HK reports to be automatically generated at a specific interval, we intend to receive the reports only when the TC with subtype 21 is send.
###### Service 8, function management service

subtype 1:

FID / 8 bits	Value / 32 bits

NAME	APP ID	FID	Value
Power / control	Generic	0: off / 1: on / 2: reset	Device id / EPS / OBC / ADCS IAC COMMS / SU GPS / SD1 / SD2
Time / control	Generic	3: Set time	time in QB50 epoch
	EPS	4: COMMS antenna deployment / 5: SU antenna deployment	time in msec / 0 for default
	COMMS	6: set rate / 7: set RX / 8: set TX	bps / 0,1: on/off / 0,1: on/off
	IAC	9: take picture	resolution / 0 for default

For power control, each subsystem should implement the actions that they can.
For the EPS the TC with FID OBC or ADCS should have the same action due the EPS hardware.
If the APP ID equals the FID, only the reset command is applicable and the subsystem should reset itself.
###### Service 13, large data transfer service

subtype TC enable, disable packet store, 1,2:
###### Service 15, mass storage service

subtype TC enable, disable packet store, 1,2:

SID / (store id) / 8 bits

subtype TC downlink contents, 9:

SID / (store id) / 8 bits	mode / 8 bits	From time / 32 bits	To time / 32 bits

subtype TC delete contents, 11:

End time / 32 bits / (if 0 delete all)	SID / (store id) / 8 bits

subtype TC report catalogue 12:

SID / (store id) / 8 bits

subtype TM packet store catalogue 13:

time from / (store id) / 32 bits	time to / (store id) / 32 bits	percentage / filled / 8 bits	percentage / downlinked / 8 bits	packets / stored / 8 bits	packets / downlinked / 8 bits

‘’BDD’’ testing scenarios

(here to describe the BDD testing scenarios)
( for more info see: https://en.wikipedia.org/wiki/Behavior_Driven_Development )

###### Coding guidelines

Variables should be in uintx_t type.

Only comments in “/**/”, never with “//”

Most functions should return a typedef enum with execution state.

typedef enum {
R_PKT_ILLEGAL_APPID	= 0,
R_PKT_INV_LEN	= 1,
R_PKT_INC_CRC	= 2,
R_PKT_ILLEGAL_PKT_TP	= 3,
R_PKT_ILLEGAL_PKT_STP	= 4,
R_PKT_ILLEGAL_APP_DATA	= 5,
R_OK	= 6,
R_ERROR	= 7,
R_EOT	= 8
}OBC_returnStateTypedef;

OBC_returnStateTypedef power_control_app(tc_tm_pkt *pkt);

indentation should be /t with 4 spaces width.

Preferable braces format.
  if (condition) {
   } else if (condition) {
   } else {
   }

All if should have braces.

Names should follow snake case.

All variables should be initialized.

In c, code should be placed in .h .c files.
In header files all code should be included in include guards.

#ifndef HEADER_H
#define HEADER_H

#endif

All of the hardware specific code should be written in a HAL layer.

void HAL_obc_SD_OFF() {
    HAL_GPIO_WritePin(GPIOB, GPIO_PIN_15, GPIO_PIN_RESET);
}