Contents

Introduction

1	Scope

2	References

3	Terms, conditions and abbreviated terms

4	Subsystems common commands
4.1	Introduction
4.2	Telecommand Boot Count Service (service <number here>)
4.3	Telecommand Event Log Request Service (service <number here>)
4.4	Telecommand Set Time Service (service <number here>)
4.5	Telecommand Subsystem Reset Service (service <number here>)

# Introduction

The LSF-SDD-* series of documents are ment to describe the communication format between the various subsystems aboard a cubesat. The various functions supported and executed by the cubesat are implemented in the form of software services as recommented from ECSS, The European Cooperation for Space Standardization and these standards and recommentations has been followed where possible and extended to mission specific areas, also followed practices from other cubesat missions has been taken into account.

# 1 Scope
This documents describes the minimal services that every subsystem across a cubesat should be able to generate a service report following a service request (services are used in accordance with their specification on reference document [i] )
# 2 References

1. ECSS-E-70-41A (30Jan2003)

# 3 Terms, conditions and abbreviated terms

# 4 Subsystems common commands

## 4.1 Introduction

The following commands are to be implemented from every subsystem on board the gr02UPSat. The packet structure (headers and data fields) for every command is displayed in this paragraph.

### 4.1.1 Telecommand packet structure
Packet Header (48 bits)					Packet Data Field (Variable bits)
Packet ID				Packet Sequence Control		Packet Length	Data Field Header (Optional see Note1)	Application Data	Spare	Packet Error Control (see Note 2)
Version Number (=0)	Type (=1)	Data Field Header Flag	Appliation Process ID
3	1	1	11	2	14
16				16		16	Variable	Variable	Variable	16

Figure 1: Telecommand packet fields
- NOTE 1, see note 1 on reference [i], page 42.
- NOTE 2, see note 1 on reference [i], page 43.
For more information regarding the individual segments of the frame see reference [i], page 42.

### 4.1.2 Telemerty source packet structure
Packet Header (48 bits)					Packet Data Field (Variable bits)
Packet ID				Packet Sequence Control		Packet Length	Data Field Header (Optional see Note1)	Source Data	Spare (Optional)	Packet Error Control (Optional)
Version Number (=0)	Type (=0)	Data Field Header Flag	Appliation Process ID	Grouping Flags	Source Sequence Control
3	1	1	11	2	14
16				16		16	Variable	Variable	Variable	(see Note 2)

Figure 2: Telemetry packet fields
- NOTE 1, see note 1 on reference [i], page 46.
- NOTE 2, see note 1 on reference [i], page 46.

### 4.1.3 Service data units
A service request or report contains the SourceData field, which is composed from the actual data called 'Service data units' that is relevant to the specific service function. The general format of a service data unit is presented next:
Parameter1	Parameter2	Parameter3
<type>	<type>	<type>

supported types are presented on reference [i], page 42.

## 4.2 Telecommand Boot Count Service
### 4.2.1 Scope / Service concept
This service request instructs the receiving subsystem to generate a service report with data payload containing the boot counter, the boot counter response contains how many times the subsystem has suffer a reset ( a counter incremented on every boot and stored localy on the subsystem )
The service data unit format is the following:
Parameter1
Unsigned Integer

### 4.2.2 Service Requests and reports
Requests:
BootCounter
0

BootCounter: 1 bit long, the zero bit to initiate a service request from the receiving subsystem.
Reports:
BootCounter
Unsigned Integer / 4 octets

BootCounter: 32 bit long, type of uint32.

### 4.2.3 Service capability sets
Minimum Capability set:
Subtype	Service request, report or capability
1
2

## 4.3 Telecommand Event Log Request Service
### 4.3.1 Scope / Service concept
This service request instructs the receiving subsystem to generate a service report with data payload containing the
The service data unit format is the following:
Parameter1

### 4.3.2 Service Requests and reports
Requests:
0

BootCounter: 1 bit long, the zero bit to initiate a service request from the receiving subsystem.
Reports:
BootCounter:

### 4.3.3 Service capability sets
Minimum Capability set:
Subtype	Service request, report or capability
1
2